## Slide 1: Quantum Crosstalk Mitigation in Multi-Tenant Computing
Presented By,
Syed Emad Uddin Shubha
CS Grad Student, LSU

## Slide 2: Crosstalk in Quantum Hardware
Crosstalk = Unintended interaction between qubits.
Causes correlated errors, breaks local noise assumption.
Sources:
Always-on ZZ interactions (superconducting qubits)
Residual XX from Molmer–Sorensen gates (trapped ions)
Frequency crowding, pulse overlap.

## Slide 3: Why Crosstalk Matters
Degrades fidelity (up to 20× error in CNOTs)
Violates assumptions in QEC
Interferes with parallelism and scheduling
In MTC, someone can abuse scheduling and degrade one’s performance.
Maybe some information leakage is possible.

## Slide 4: Quantum Crosstalk Mitigation
General Methods
Gate Reordering
Cycle-Aware Scheduling (CYCO)
Multi-Tenant Systems
Qubit Allocation Optimization using RL
Employing Spectator Qubits
More possible solutions:
Quantum Differential Privacy
Probabilistic Error Cancellation

## Slide 5: Gate Reordering Based on Commutativity
Exploit commutativity of quantum gates (e.g., CNOTs, SWAPs).
Reorder instructions to avoid simultaneous execution of high-crosstalk gates.
3. Uses bidirectional algorithm:
  Forward pass → look ahead for interference
  Backward pass → adjust past gates
4. Avoids serialization → retains parallelism
5. Up to 18% fidelity gain on average over naive scheduling

## Slide 6: Cycle-Aware ZZ Crosstalk Mitigation (CYCO)
* Problem with naive schedulers:
  Insert barriers to isolate gates → hurts parallelism
  Ignores gate duration and quantum clock cycles
CYCO Approach:
Models active-qubit interference and cross-qubit interference
Schedules gates in cycle windows using new data structure: TDDG (Time and Distance Dependency Graph)
Dynamically inserts/removes barriers
Result: Up to 37% reduction in program cycles, maintains fidelity on IBMQ-Brisbane & Google Bristlecone

## Slide 7: RL-Based Qubit Allocation for MTC
In quantum networks (or shared QPUs), qubit reuse creates resource contention + dynamic crosstalk patterns. Hence:
Model as MDP → Optimize expected fidelity + waiting time
Combine Reinforcement Learning with Active Learning to reduce training cost
Learns to dynamically allocate qubits based on:
Fidelity maps, Wait time, Resource occupancy
Impact:19.2% better path maturity & 23.5ms lower average waiting time

## Slide 8: Spectator Qubits for Real-Time Calibration
Errors drift over time, frequent recalibration interrupts computations. Hence:
Reserve spectator qubits to monitor coherent errors (e.g., magnetic field drift, crosstalk)
Use this info to adapt control strategies (e.g., over-rotation angle)
Fisher Information and Cramér–Rao bound determine how fast spectator qubits can estimate error parameters.

## Slide 9: Quantum Differential Privacy (QDP)
Treat crosstalk as a leaky quantum channel
Use hockey-stick divergence to bound distinguishability from neighboring inputs
Helps design:
  Privacy-aware schedulers
  Leakage-tolerant QEC schemes
  Noise shaping for privacy

## Slide 10: Probabilistic Error Cancellation (PEC)
PEC is a zero-noise extrapolation technique.
Model crosstalk-affected gate as a noisy channel.
Decompose into ideal + error operations, sampled via quasi-probabilities.
It uses Gate Set Tomography (GST) to learn how each gate deviates from the ideal.
GST process can be extended to include correlated gate pairs.

## Slide 11: Research Ideas
We might combine these ideas but still need a better way to proceed.
References:
https://github.com/syedshubha/CrosstalkMTC